## Slide 1: Why redesign RAPID?
Race conditions in microarchitecture.
High CPI and high latency
Could not meet power requirements with realized CPI

## Slide 2: Changes in RAPID-X
Moved most of logic from state machine to combinational
Resolved race conditions
Implemented forwarding and hazard unit.

## Slide 3: Frequency and Power Requirement
Reduced core clock speed requirement from ~400 MHz to ~135 MHz
Chart: Power Improvement
| RAPID | RAPID-X
 | 1.1 | 0.25
 | 0 | 0

## Slide 4
Chart: IPC
| SumXOR_Loop | BitRotation_Test | NestedAdd_Loop | ArithmeticProgression_Sum
RAPID-X | 0.88231 | 0.89996 | 0.81831 | 0.85712
Reference | 0.71429 | 0.75 | 0.42918 | 0.66668
RAPID | 0.2941 | 0.29998 | 0.27276 | 0.2857

## Slide 5
Chart: IPC Uplift in Percent
| SumXOR_Loop | BitRotation_Test | NestedAdd_Loop | ArithmeticProgression_Sum
RAPID-X | 300.0079 | 300.0067 | 300.0123 | 300.0096
Reference | 242.8758 | 250.0156 | 157.3484 | 233.3514
RAPID | 100 | 100 | 100 | 100

## Slide 6
Chart: 100 MIPS Clock Frequency (MHz)
| SumXOR_Loop | BitRotation_Test | NestedAdd_Loop | ArithmeticProgression_Sum
RAPID-X | 113 | 111 | 122 | 117
Reference | 140 | 133 | 233 | 150
RAPID | 340 | 333 | 367 | 350

## Slide 7
Chart: Pipeline Latency
| Cycles
RAPID-X | 3
RAPID | 12