## Slide 1: NG iDesign Team Phase 1
Team Members: Youssef Samwel, Nicolas Sayeed, Pablo Rodriguez, Davi Dantas, Evan Kasky, Timothy Ogg
Advisors: Dr. Mike Borowczak and Dr. Chung Yong Chan

## Slide 2: Project Overview
Design an ASIC implementing the RISC-V RV32I base instruction set, except for memory ordering and environment/system calls.
Perform functional and/or formal verification of the design to confirm functionality of the design. Use the Universal Verification Methodology (UVM) standardized methodology. Target a minimum of 85% code coverage.
Synthesize the hardware description language into a netlist for physical layout. Target the 45nm FreePDK45 technology using the Nangate open cell library.
The design should be capable of processing 100 million instructions per second (100 MIPS) within the operating range of 0.95-1.25V and 0-125°C and consume a maximum of 1W. Additionally, the design should incorporate an L1 cache of at least 16MB.
Test the performance and system-level functionality of the design by creating and executing test cases in RV32I assembly.

## Slide 3: Teams Dynamics
Design Team – Youssef & Nicolas
  System Design
  Established modular requirements
  Worked on redesigns
Memory Team – Pablo & Timothy
  Worked on establishing the cache subsystem
  Established functionality of IF & MEM
  Testing of memory stage
Verification Team – Davi & Evan
  Verified essential units; Execution & Decoder
  Worked on early UVM reports & Assertion-based Testbenches

## Slide 4: Summary of Design Requirements
Simple RTL logic
Support the 37 RISC instructions
Use the classic 5-stage pipeline

## Slide 5: RAPID Core

## Slide 6: RAPID Core – MEM FSM

## Slide 7: Feedback from Early Testing
Development of testbenches
Inspection of Architecture
Performance

## Slide 8: Why redesign RAPID?
Race conditions in microarchitecture.
High CPI and high latency.
Could not meet power requirement with realized CPI.

## Slide 9: RAPID-X Core
4-Stage Pipeline
Optimized FSM
Combinational logic
Resolve Race Conditions

## Slide 10: RAPID-X Core

## Slide 11: Frequency and Power Requirement
Reduced core clock speed requirement from ~350 MHz to ~115 MHz

## Slide 12
Chart: IPC Uplift in Percent
| SumXOR_Loop | BitRotation_Test | NestedAdd_Loop | ArithmeticProgression_Sum
RAPID-X | 300.0079 | 300.0067 | 300.0123 | 300.0096
Reference | 242.8758 | 250.0156 | 157.3484 | 233.3514
RAPID | 100 | 100 | 100 | 100

## Slide 13
Chart: Pipeline Latency
| Cycles
RAPID-X | 3
RAPID | 12

## Slide 14: Cache Subsystem
16 MB L1 Cache
Split cache D-Cache & I-Cache
Direct Mapped
Modular cache for instantiation
Initial Block Diagram

## Slide 15: Cache Subsystem
Cache module is instantiated separately for the I-Cache and D-Cache
Better code re-usability
Per-cache optimization (size, associativity) using instance parameters
Simulated memory is initialized at startup

## Slide 16: Cache Subsystem
Simple ready/valid protocol provides robust synchronization and signaling between cache subsystem and CPU pipeline.
Cache utilizes two (very fast) SRAM blocks internally.

## Slide 17: Cache signals in waveform viewer

## Slide 18: Cache and fake memory simulation log

## Slide 19: Instruction Fetch Testing
Preload sequence of instructions
Validate FSM transitions, PC updates, and cache communication
Simulate edge cases
Sequential fetching when the pipeline ready flag is 1
Produce a no op for memory stalls
Correct synchronization with pipeline and accurate instructions delivery

## Slide 20: Testing Waveforms and logs

## Slide 21: Testing Waveforms and logs

## Slide 22: Testing Waveforms and logs

## Slide 23: Verification

## Slide 24: Platform
Link
EDA Playground

## Slide 25: Obstacles
Learning Curve
Crawl, Walk, Run – Building blocks
Code Dependency – Execute Stage
Adapt to module updates

## Slide 28: Results Examples
ADDI
ADD
AND
SLTI

## Slide 29: Obstacles
UVM Learning Curve
  Understanding UVM concepts such as sequences, agents, and virtual interfaces was a long process
  Initially not knowing if my lack of UVM knowledge was the reason for failure or there was an issue with the design
Core / Signal Redesign
  Adapting existing testbenches to the new design requires significant time
  Adds lengthy debug process to find errors where existing testbench gives an error

## Slide 30: Custom Instruction Generator
Custom SystemVerilog module to generate random valid instructions
  Outputs a random valid 32-bit RISC-V instruction
  Generates valid random data depending on the instruction type
  Properly encodes(combines) the bits into a 32-bit instruction
Still working on integrating into existing UVM testbench

## Slide 31: Initial Instruction Decoder UVM
Learning and Resources
    Watched Cadence UVM training modules for foundational understanding.
    Watched other UVM training resources online
Progress
    Framework for the decode stage of the UVM testbench has been set up.
    Basic testbench infrastructure is operational.
Current Gaps
    Custom instruction generator is developed but not yet integrated into the testbench/DUT.
    DUT is not producing the correct iop signals as expected.
Next Steps
    Integrate the custom instruction generator with the UVM testbench.
    Debug and fix the issue in the DUT logic affecting the iop signal generation.
    Ensure all instructions are properly being decoded

## Slide 32: Test Program: Fib Gen
addi x5, x0, 0 # F0
addi x6, x0, 1 # F1
addi x7, x0, 20 # Number of iterations
loop:
add x8, x5, x6 # F_next = F0 + F1
addi x5, x6, 0 # F0 = F1
addi x6, x8, 0 # F1 = F_next
addi x7, x7, -1
bne x7, x0, loop

## Slide 33: Test Program: Fib Gen

## Slide 34: Benchmark: XOR LOOP
SumXOR_Loop |  |  | 
Metric | X | Reference | RAPID
Time | 113352 | N/A | 340065
Clocks | 56676 | 70008 | 170032.5
Instr | 50,006 | 50,006 | 50,006
CPI | 1.133383994 | 1.399992001 | 3.400241971
IPC | 0.882313501 | 0.714289795 | 0.294096717
% Up | 300.0079399 | 242.8758142 | 100
Freq | 113 | 140 | 340
li t0, 0 # Initialize sum to 0
li t1, 0 # Initialize XOR result to 0
li t2, 10000 # Loop counter (large number)
li t3, 1 # Increment value
loop:
add t0, t0, t3 # Add increment to sum
xor t1, t1, t3 # XOR current value with t1
addi t3, t3, 1 # Increment current value
addi t2, t2, -1 # Decrement loop counter
bne t2, x0, loop # Repeat if counter not zero
nop

## Slide 35
Chart: IPC Uplift in Percent
| SumXOR_Loop | BitRotation_Test | NestedAdd_Loop | ArithmeticProgression_Sum
RAPID-X | 300.0079 | 300.0067 | 300.0123 | 300.0096
Reference | 242.8758 | 250.0156 | 157.3484 | 233.3514
RAPID | 100 | 100 | 100 | 100

## Slide 36: Management Tools
AGILE Methodology
Regular weekly meetings
Established collaborative spaces
  Discord
  GitHub
  OneDrive
Followed timelines to meet milestones

## Slide 37: Plan for Phase 2
Finalize functional and/or formal verification of the design, adhering to the target code coverage.
Use electronic design tools to perform physical design and create a layout of the design.
Conduct static timing analysis (STA), IR drop, and electromigration analysis to ensure physical performance requirements are met. Target a maximum IR drop of 5% with no timing failures and maximum current density within limits.
Use physical design techniques such as design rule checking (DRC) to establish design manufacturability and layout versus schematic (LVS) to ensure correctness of the physical design.

## Slide 38: THANK YOU FOR THE SUPPORT!!!